ZM－R380B  Main Features

specifications and technical parameters：

| 1 | Total Power | 3200W |
| --- | --- | --- |
| 2 | Top heater | 800 W |
| 3 | Bottom heater | Infrared plate 2400 W |
| 4 | Power supply | AC 220V ± 10% - 50/60Hz |
| 5 | Dimensions | 445×430×500mm |
| 6 | Positioning | V-groove, PCB support can be adjusted in any direction and with external universal fixture |
| 7 | Temperature control | K-type thermocouple (Closed Loop), heating independently, the precision is ±3 degree |
| 8 | PCB size | Max 310×300mm Min 20×20 mm |
| 9 | Net Weight | 25 kg |

Product specification

1、The bottom is IR heater; The top is hot-air heater.

2、Choose imported high-precision materials (temperature sensor, PLC, heater) to control the BGA desoldering & soldering procedures precisely. 3、This machine has a computer communications function, built-in PC serial port, external temperature interface with software to achieve computer control;

4、High-precision thermocouple to achieve the precise temperature detection;

5、The top and bottom heater work independently. A cross-flow fan cools rapidly to protect the PCB from deformation when welding.

6、Use a V-groove support equipped with a flexible fixture for PCB positioning to protect the PCB.

7、For large thermal capacity of PCB or other high-temperature and lead-free welding requirements, all can be handled easily. 8、With hot-air flow adjust device, to improve the welding effect of BGA.